## Slide 2: Control – Inputs
Inputs:
Clk – The system clock.
Reset – Active low asynchronous reset.
[2:0]Mode – The current work mode.
Sync – New line signal.
f_Sync – Start the normal mode counter.
EndFrame – The frame has ended once the 5bitCounter counted 24 lines.
EndLine – The line has ended once the 12bit counter counter either 1290 in test mode or 4096 in normal mode.
[1:0]X - Choose gap between numbers at the same row .

## Slide 3: Control - Outputs
The possible output values:
NewLine – Send a signal to the 5bitCounter when a new line has started.
Binary_or_Gray – Choose whether the output will be in Gray code or Binary code. ‘1’ for Gray and ’0’ for Binary.
[2:0]Xmode - The gap between numbers at the same row for the Counter :
’000’: The gap between numbers at the same row will be 0.
‘001’: The gap between numbers at the same row will be 1.
‘010’: The gap between numbers at the same row will be 4.
‘011’: The gap between numbers at the same row will be 8.
‘100’: Change between 12’b0 and 12’b1 every clock cycle.
’110’: Change between 12’b0 and 12’b1 every other clock cycle.
Test – ‘0’ for the 12bitcounter to count to 4095 and ‘1’ for the 12bitCounter to count to 1289
Load – ’1’ to load a 12bit value to the counter
5b_enb – ‘1’ active, ‘0’ inactive with ‘0’ at all outputs
12b_enb - ‘1’ active, ‘0’ inactive with ‘0’ at all outputs
Cnt_enb - ‘1’ active, ‘0’ inactive with ‘0’ at all outputs
FV_enb - ‘1’ active, ‘0’ inactive with ‘0’ at all outputs
Delta – ‘1’ to add deltaY to the count
[1:0]ValSel – ’00’ for FV, ‘01’ for [11:0]Val and ’10’ for 12’b1

## Slide 5: Normal work mode – [2:0]Mode = ‘001’
READY
[2:0]Mode == ‘001’ :
5b_enb =‘1’
Test = ‘0’
Binary_Or_Gray=’1’
NewLine =‘1’(2d clock)
FV_enb =’0’
Load=’0’
Normal:
Input:
EndLine=’0’:
Output:
Xmode= ‘001’
Cnt_enb=‘1’
12b_enb = ‘1’
Input:
EndLine=’1’:
Output:
Cnt_enb=‘0’
12b_enb = ‘0’
Sync=‘1’
2 clock
IDLE
EndLine=‘1’
EndFrame=‘1’

## Slide 6: Constant test mode – [2:0]Mode = ‘010’
READY
[2:0]Mode == ‘010’ :
5b_enb =‘1’
Test = ‘1’
Binary_Or_Gray=’0’
NewLine =‘1’(2d clock)
FV_enb =’0’
[1:0]ValSel = ‘01’
Load=’1’(2d clock)
Cnt_enb=‘1’
Xmode= ‘000’
Normal:
Input:
EndLine=’0’:
Output:
Xmode= ‘000’
Cnt_enb=‘1’
12b_enb = ‘1’
Input:
EndLine=’1’:
Output:
Cnt_enb=‘0’
12b_enb = ‘0’
Sync=‘1’
2 clock
IDLE
EndLine=‘1’
EndFrame=‘1’

## Slide 7: Checkerboard 1x1’white’– [2:0]Mode = ‘011’
READY
[2:0]Mode == ‘011’ :
5b_enb =‘1’
Test = ‘1’
Binary_Or_Gray=’0’
NewLine =‘1’(2d clock)
FV_enb =’0’
Load=’1’(2d clock)
Cnt_enb=‘1’
Xmode= ‘000’
Input: Flag = ‘0’:
Output: [1:0]ValSel = ‘00’
Input: Flag = ‘1’:
Output: [1:0]ValSel = ‘10’
CB 1x1:
Input:
EndLine=’0’:
Output:
Xmode= ‘100’
Cnt_enb=‘1’
12b_enb = ‘1’
Flag = ~Flag(1clk)
Input:
EndLine=’1’:
Output:
Cnt_enb=‘0’
12b_enb = ‘0’
Sync=‘1’
2 clock
IDLE
EndLine=‘1’
EndFrame=‘1’

## Slide 8: Checkerboard 1x1’black’– [2:0]Mode = ‘100’
READY
[2:0]Mode == ‘100’ :
5b_enb =‘1’
Test = ‘1’
Binary_Or_Gray=’0’
NewLine =‘1’(2d clock)
FV_enb =’0’
Load=’1’(2d clock)
Cnt_enb=‘1’
Xmode= ‘000’
Input: Flag = ‘0’:
Output: [1:0]ValSel = ‘10’
Input: Flag = ‘1’:
Output: [1:0]ValSel = ‘00’
CB 1x1:
Input:
EndLine=’0’:
Output:
Xmode= ‘100’
Cnt_enb=‘1’
12b_enb = ‘1’
Flag = ~Flag(1clk)
Input:
EndLine=’1’:
Output:
Cnt_enb=‘0’
12b_enb = ‘0’
Sync=‘1’
2 clock
IDLE
EndLine=‘1’
EndFrame=‘1’

## Slide 9: Checkerboard 2x2 ’white’– [2:0]Mode = ‘101’
READY
[2:0]Mode == ‘101’ :
5b_enb =‘1’
Test = ‘1’
Binary_Or_Gray=’0’
NewLine =‘1’(2d clock)
FV_enb =’0’
Load=’1’(2d clock)
Cnt_enb=‘1’
Xmode= ‘000’
Input: Flag = ‘00’ or ‘01’:
Output: [1:0]ValSel = ‘00’
Input: Flag = ’10’ or ‘11’:
Output: [1:0]ValSel = ‘10’
CB 2x2:
Input:
EndLine=’0’:
Output:
Xmode= ’110’
Cnt_enb=‘1’
12b_enb = ‘1’
Flag = Flag+1(1 clk)
Input:
EndLine=’1’:
Output:
Cnt_enb=‘0’
12b_enb = ‘0’
Sync=‘1’
2 clock
IDLE
EndLine=‘1’
EndFrame=‘1’

## Slide 10: Checkerboard 2x2’black’– [2:0]Mode = ‘110’
READY
[2:0]Mode == ‘110’ :
5b_enb =‘1’
Test = ‘1’
Binary_Or_Gray=’0’
NewLine =‘1’(2d clock)
FV_enb =’0’
Load=’1’(2d clock)
Cnt_enb=‘1’
Xmode= ‘000’
Input: Flag = ‘00’ or ‘01’:
Output: [1:0]ValSel = ‘10’
Input: Flag = ‘10’ or ‘11’:
Output: [1:0]ValSel = ‘00’
CB 2x2:
Input:
EndLine=’0’:
Output:
Xmode= ‘110’
Cnt_enb=‘1’
12b_enb = ‘1’
Flag = Flag+1(1clk)
Input:
EndLine=’1’:
Output:
Cnt_enb=‘0’
12b_enb = ‘0’
Sync=‘1’
2 clock
IDLE
EndLine=‘1’
EndFrame=‘1’

## Slide 11: Extracting Ramp - [2:0]Mode = ‘111’
READY
[2:0]Mode == ‘111’ :
5b_enb =‘1’
Test = ‘1’
Binary_Or_Gray=’0’
NewLine =‘1’(2d clock)
FV_enb =’1’
Load=’1’(2d clock)
Cnt_enb=‘1’
Xmode= ‘000’
[1:0]ValSel = ‘00’
Input: Flag = ‘0’:
Output: delta = ‘0’
Input: Flag = ‘1’:
Output: delta = ‘1’(1st clk)
Ramp
Input:
EndLine=’0’:
Output:
Xmode= ‘110’
Cnt_enb=‘1’
12b_enb = ‘1’
Flag = 1
Input:
EndLine=’1’:
Output:
Cnt_enb=‘0’
12b_enb = ‘0’
Sync=‘1’
2 clock
IDLE
Flag = 0
EndLine=‘1’
EndFrame=‘1’